## Slide 1: PDR Electrical Power System with Maximum Power Point Tracking (MMPT)
Lead Engineer: Elijah Gibbs
Manager: Jeffrey Kruth
Technical Advisor: Nate Fite

## Slide 2: Project Description
Design and Test a full electrical power system(EPS) for a CubeSat
  The project will encompass all steps of the EPS from input specifications to output considerations
  Will also consider the implementation of an MPPT input design.
Goal is to have this design function for a 1U-3U CubeSat

## Slide 3: System Level Design
There will be two boards:
  A board for the batteries and battery management
  A board for all other EPS functions:
    MPPT
    BCR
    Output Regulation
    Microcontroller

## Slide 4: Software Flowchart

## Slide 5: MPPT
MPPT can intake:
  An input voltage range up to 30v
  An input current range up to 20A
System will use FET to traverse the I-V curve.
Will use perturb and observe method find peak power

## Slide 6: Battery Charge Regulator
Will utilize buck/boost setup to convert power to battery level
Will switch between buck and boost convertor depending on needed power input needs
Will use Zener Diode to stop overvoltage spike
Will use fuse to stop overcurrent spikes
Will use comparator setup to detect when to stop charging

## Slide 7
LtSpice Buck Convertor
Tested over several cases all cases can be adjusted to within 8.4V
No major anomalies to contend with

## Slide 8: LtSpice Boost Convertor
Tested over several cases all cases can be adjusted to within 8.4V
Voltage spike on 1V is tolerable due to Zener diode voltage clamp after boost convertor.
May also look to add capacitor before inductor to reduce overvoltage spike.

## Slide 9: Battery Layout
Will utilize two series setup.
4.2V batteries at 5000mAhrs will provide 42Whrs of power
HZ-2S-A10 will function as a Battery Management System Protection Board

## Slide 10: Regulated Lines/Output
Will provide regulated output using switching regulated buck and boost convertor ICs.
Lines available 3.3V @ 1A, 5V @ 1A, 12V @ 1A, Battery Voltage.
Will include switches to turn off individual lines to conserve power when needed.
For testing output can use a programable DC load

## Slide 11: Microcontroller
SEEED STUDIO XIAO RP2040
  ARM® Cortex®-M0+
  2 Cores in CPU
Clock Speed is 48MHz
Normal Current: 28.9 mA
Functions
  Monitor voltages at key points in system
  Adjust voltages through PWM channels to FETS

## Slide 12: Main PCB Layout
Size will me 90mm x 90mm
Path widths:
  0.508mm for data lines
  1-2mm for power lines
2oz/sqft of copper
2 layers PCB

## Slide 13: Fusion Model
Current Models on Left
Fabrication will be done in house at the space science center for the first few prototypes will be using RO4003C from Rogers Corp.
Final design will be manufactured from company – PCBWay
Will have a battery board and an main EPS board.

## Slide 14: Project Requirements
  Build an EPS that shall:
  Generate power from solar array
  Utilizes a MPPT structure to allow for maximum power to be gathered
  Regulate power going in and out of the batteries
  Take power from batteries and regulates it to a 3.3V regulated line, 5V regulated line and 12V regulated line.
  Ensure power is distributable to multiple other systems
  Have onboard microcontroller to control and monitor EPS with sensors

## Slide 15: Resources
Parts: Suppliers like DigiKey, Mouser Electronics, and free sampling from Coilcraft, KEMET, STmicro, TI, Rogers, etc.
Software: LTspice (circuit simulation), draw.io (circuit and block diagram design), Fusion 360 (3D modeling/PCB design), Python (programming).
Tools: Soldering iron, oscilloscope, multimeter, current supply, DC load, and general electric items (available in SSC labs).

## Slide 16: Risks
Technical:
Heat distribution
Current/Voltage limits
Generating Electric/Magnetic Fields
Electrostatic Shock
Requitements that need to be met
Programmatic:
Acquiring parts/Replaceability
  Part Costs
  Lead Times
Items that slow down the project

## Slide 17: Budget
Overbudget slightly due to buying extra spares.
  Will allow for mistakes to be made in prototyping
Direct Cost |  |  |  |  |  |  |  |  |  |  | Indirect Cost |  |  |  | 
Labour |  |  |  |  | Materials Cost |  |  |  |  |  | Items: | Office Supplies | Building Costs | Licenses | Other
Title | Hourly Wage ($) | Hours | Total Cost |  | Task | Progress | Expected Cost | Actual Cost | Under/Over |  | Budgeted: | 2500 | 10000 | 1000 | 
Project Lead Engineer | 40 | 91 | 3640 |  | MPPT | Complete | 20 | 10.8834 | -9.1166 |  | Actual | 2500 | 10000 | 545 | 
Technical Advisors | 100 | 11 | 1100 |  | Batteries | Complete | 25 | 19.749 | -5.251 |  | Under/Over | 0 | 0 | -455 | 0
Project Manager | 120 | 10 | 1200 |  | Battery Regulators | Complete | 15 | 10.086 | -4.914 |  | Total | 13045 |  |  | 
 |  | Total of All | 5940 |  | Output Regulators | Complete | 10 | 8.1052 | -1.8948 |  |  |  |  |  | 
 |  |  |  |  | Microcontroller/Supporting | Complete | 30 | 23.46 | -6.54 |  |  |  |  |  | 
 |  |  |  |  | Spare Parts | Complete | 100 | 130.6064 | 30.6064 |  |  |  |  |  | 
Total Costs of Project ($): | 19187.89 |  |  |  | Total Actual Cost |  | 200 | 202.89 | 2.89 |  |  |  |  |  | 

## Slide 18: Timeline / Endpoint
Estimate for time to complete was at roughly 240 hours, Currently have spent 91 hours in total.

## Slide 19: Endpoint/Going Forward
Next Steps:
  Manufacture PCB
  Populate and Test PCB
  Start Iteration Processes
Endpoint :
  The endpoint of this project is to be a functional brass board and PCB design.

## Slide 20: Questions?

## Slide 21: Unused Slides Below

## Slide 22: Why am I qualified to do this?
Applicable Experience:
  Worked as Embedded HW Engineer Intern over the summer
    Have enhanced my knowledge in electrical systems
    Have enhanced my knowledge in software systems
Education:
  Space Systems Engineering
    Gained a fundamental understanding of electrical systems within the context of space technology.
      Through classes such as: Circuits, Spacecraft Electronic Systems, RF Transmission Lines & Circ.
  Minor in Computer Science:
    Gained hands-on experience in coding, software design, and problem-solving.
Overall:
  With all these areas combined I have acquired a well-rounded skill set capable of taking on the challenges of this project.
Notes: Mention Classes